EMERGENCY ALERT SYSTEM (EAS)

PROCEDURES FOR THE

JUNEAU LOCAL AREA

I. 	INTRODUCTION

This Emergency Alert System (EAS) Local Area Plan was developed by the Juneau Local Area Emergency Communications Committee in cooperation with local broadcast and cable operators, the National Weather Service, and the City and Borough of Juneau. The Plan outlines the methods used to disseminate emergency information and warning to the general public in the Juneau EAS Local Area or any portion thereof, within the broadcast coverage and cable system service areas, at the request of local, State and Federal officials. This local EAS plan may be activated in response to common local emergency situations such as power outages, floods, civil disorders, earthquakes, heavy snows, toxic chemical leaks or any occurrence which poses a danger to life or property.

Acceptance of/or participation in this plan shall not be deemed as a relinquishment of program control, and shall not be deemed to prohibit a broadcast licensee or cable operator from exercising his independent discretion and responsibility in any given situation. Broadcast stations and cable systems originating emergency communications shall be deemed to have conferred rebroadcast authority. The concept of management of each broadcast station and cable system to exercise discretion regarding the transmission of emergency information and instructions to the general public is provided by the FCC Rules and Regulations.

II. 	AUTHORITY

Title 47 U.S.C. 151, 154 (i) and (o), 303 (r), 524(g) and 606; and 47 C.F.R. Part 11, FCC Rules and Regulations, Emergency Alert System (EAS)

III. 	KEY EAS SOURCES

A.	Local Primary Source (LP-1)

| Location | KINY-AM 800 KHz |
| --- | --- |
| EAS Codes in Encoder/Decoder | See Annex D |
| EAS Monitoring Assignments | ARCS, NWS, KTOO |
| Contact | Dennis Egan |
| Telephone | 907-586-1800 |
| Unlisted Telephone |  |
| Hours of Operation | 24 hrs / 7days (Unattended 12:00 AM to 3:00 AM / Weekends 4:00 PM to 6:00 AM) |
| Communications Facilities | 1107 W. 8th Street |
| Administrative E-mail | egan@ptialaska.net |

B.	Local Primary Source (LP-2)

| Location | KTOO – FM 104.3 MHz |
| --- | --- |
| EAS Codes in Encoder/Decoder | See Annex D |
| EAS Monitoring Assignments | KINY, NWS, ARCS |
| Contact | Bill Legere |
| Telephone | 907-586-1670 |
| Unlisted Telephone |  |
| Hours of Operation | 24 hrs / 7 days (Unattended 12:00 AM to 5:00 AM) |
| Communications Facilities | 360 Egan Drive |
| Administrative E-mail | bill@ktoo.org |

C.	Local Primary Source (LP-3)

| Location | NOAA Weather Radio 162.400 MHz -162.55 MHz Primary |
| --- | --- |
| EAS Codes in Encoder/Decoder | See Annex D |
| EAS Monitoring Assignments | N/A |
| Contact | Joel Curtis |
| Telephone | 907-790-6803 |
| Unlisted Telephone |  |
| Hours of Operation | 24 hrs / 7 days |
| Communications Facilities | 8500 Mendenhall Loop Road |
| Administrative E-mail | Joel.curtis@noaa.gov |

IV. 	IMPLEMENTATION

The following procedures should be used to implement EAS alerts.

A. 	Procedures for Designated Officials

1.	 Activation Request

Request activation of the EAS facilities through the NWS Juneau Forecast Office via phone or other available communications facilities.  The Juneau Forecast Office may call back the requesting agency to verify authenticity of the request.

In the event the NWS Juneau Forecast office cannot activate the EAS facilities, request activation of the EAS facilities through the LP-1 or LP-2 via phone or other available communications facilities.

2. 	Contact Format

Designated officials use the following format when contacting the key EAS sources:

"This is (Name/Title) of (Organization). I request that the Emergency Alert System be activated for the Juneau area because of (Description of emergency)."

3. 	Details of Transmission

Designated officials and/or EAS source personnel determine transmission details (i.e., live or recorded, immediate or delayed). Officials should provide emergency program material including a description of the emergency, actions being taken by local government, and instructions to the public.

4.	Lines of Communication

Keep line of communication open if necessary.

5.	Specific Area Activation

For a unique emergency not involving the entire Juneau local area, local authorities may request activation of the EAS through the broadcast station and cable system serving only the affected area.

B. 	Procedures for Broadcast and Cable System Personnel

1.	LP-1 Response to EAS Alert

Upon receipt of a request to activate the local EAS from appropriate authority, the LP-1 (or alternate LP-2) may proceed as follows:

a.	ANNOUNCEMENT

Broadcast the following announcement:

"WE INTERRUPT THIS PROGRAM BECAUSE OF A LOCAL EMERGENCY. IMPORTANT INFORMATION WILL FOLLOW."

b.	TRANSMISSION OF EAS CODES

Transmit the EAS header codes and Attention Signal.

c.	ANNOUNCEMENT

Transmit the following announcement and material:

"WE INTERRUPT THIS PROGRAM TO ACTIVATE THE EMERGENCY ALERT SYSTEM FOR THE JUNEAU LOCAL AREA BECAUSE OF A LOCAL EMERGENCY. IMPORTANT INSTRUCTIONS WILL FOLLOW."

*** Follow with emergency program ***

d.	TERMINATION

To terminate the EAS message (immediately or later), make the following announcement:

“THIS CONCLUDES EAS PROGRAMMING. ALL BROADCAST STATIONS AND CABLE SYSTEMS MAY NOW RESUME NORMAL OPERATIONS."

e.	END-OF-MESSAGE CODE

Transmit the EAS End of Message (EOM) code.

Important Note: For State and local emergencies, broadcasters and cable operators have the option of transmitting only the EAS header and EOM codes without an audio emergency message. This is acceptable so that EAS coded messages can be unobtrusively relayed through areas unaffected by the emergency.

2.	Procedures for Monitoring Stations and Cable Systems

All other broadcast stations and cable systems are monitoring key sources via EAS monitor receiver/decoders and will be alerted by the header codes and attention signal. Each station and cable system upon receipt of the signal will, at the discretion of management, perform the same procedures as in step 1 above by transmitting the emergency message from the LP-1 or LP-2.

3.	 Responsibility to Provide Confirmed Information

To avoid unnecessary escalation of public confusion, all stations and cable systems must be cautious in providing news and information pertaining to the emergency. All messages must be based on definite and confirmed facts. The public must not be left to decide what is or is not fact.

4.	Resume Normal Programming

Upon completion of the above transmission procedures, resume normal programming. Appropriate notations should be made in the station and cable system records. A very brief summary may be sent to the FCC for information purposes only.

V. 	TESTS

Closed-circuit Required Weekly Tests are sent by each participating radio, television, cable system, and the National Weather Service. In addition, the Juneau LECC will schedule a “live” test of the EAS system for the Juneau area annually (utilizing the CEM “Civil Emergency Message” event code).

VI. 	ANNEXES

ANNEX A	List of designated officials

ANNEX B	Approvals

ANNEX C	List of EAS codes transmitted by key EAS sources

ANNEX D	List of broadcast stations and cable systems

ANNEX E	Juneau Area Local Emergency Communications Committee

ANNEX F	Acronyms

OPERATOR PLEASE POST

ANNEX A

DESIGNATED OFFICIALS AUTHORIZED TO ACTIVATE THE JUNEAU AREA EAS

City Manager, City and Borough of Juneau

Emergency Programs Manager, City and Borough of Juneau

Chief, Capital City Fire Rescue

Chief, Juneau Police Department

National Weather Service Forecast Office Juneau

Emergency Coordinator, Alaska Electric Light & Power

ANNEX B

APPROVALS

This Juneau EAS Local Area plan was developed and approved by the Juneau EAS Local Emergency Communications Committee.

The plan is coordinated with and distributed to all designated officials listed in Annex A and all broadcast stations and cable systems listed in Annex E.

___________________________	_________

Dennis Egan				Date

Juneau LECC Chair

___________________________	_________

Warren Russell				Date

GCI Cable

___________________________	_________

Tom Ainsworth				Date

National Weather Service

___________________________	_________

Rod Swope				Date

City and Borough of Juneau

___________________________	_________

Scott Willis				Date

Alaska Electric Light and Power

ANNEX C

LIST OF EAS CODES TRANSMITTED BY EAS KEY SOURCES

| Key EAS Source (County FIPS #) | ORG - Originator | EEE - Event |
| --- | --- | --- |
| Local Codes |  |  |
| 002110 | CIV/WXR | CEM Civil Emergency Message |
| 002110 | CIV/WXR | HMW Hazardous Materials Warning |
| 002110 | CIV/WXR | TOE 911 Telephone Outage Emergency |
| Weather Codes |  |  |
| 002110 002110 | WXR WXR | BZW Blizzard Warning AVW Avalanche Warning |
| 002110 | WXR | CFW Coastal Flood Warning |
| 002110 | WXR | TOR Tornado Warning |
| 002110 | WXR | FFW Flash Flood Warning |
| 002110 | WXR | FLW Flood Warning |
| 002110 | WXR | SVR Severe Thunderstorm Warning |
| 002110 | WXR/CIV | TSW Tsunami Warning |
| State Codes |  |  |
| 002000 | CIV/WXR | TSW Tsunami Warning |
| 002000 | CIV | CAE Child Abduction Emergency (Amber Alert) |
| 002000 | CIV | RMT Required Monthly Test |
| 002000 | CIV | ADR Administrative Message |
| National/Presidential Codes |  |  |
| 002000 | EAN | EAN Emergency Action Notification (National Only) |
| 002000 | EAN | EAT Emergency Action Termination (National Only) |

ANNEX D

JUNEAU AREA BROADCAST STATIONS AND CABLE SYSTEMS

Owner: Alaska-Juneau Communications, Inc. Stations: KINY-AM 800 (LP-1), KSUP-FM 106.3 Address: 1107 West 8th, Suite 2, Juneau, AK 99801 Phone: 907-586-1800

Owner: Capital Community Broadcasting, Inc. Stations: KTOO-FM 104.3 (LP-2), KTOO-TV3, KXLL-FM 100.7, KRNN-FM 102.7 Address: 360 Egan Drive, Juneau, AK 99801-1748 Phone: 907-586-1670

Owner: Alaska Broadcast Communications, Inc. Stations: KTKU-FM 105.1, KJNO-AM 630 Address: 3161 Channel Drive, Suite 2, Juneau, AK 99801 Phone: 907-586-3630

Owner: GCI Cable, Inc. Stations: GCI Cable Television Address: 3161 Channel Drive, Suite 1, Juneau, AK 99801 Phone: 907-586-3320

Owner: KATH -TV Stations: KATH-TV5 Address: 1107 West 8th, Suite 1, Juneau, AK 99801 Phone: 907-586-8384

Owner: Smith Media, LLC Stations:KJUD-TV8 Address: 175 South Franklin Street, Juneau, AK 99801 Phone: 907-586-3145

Owner: Gastineau Broadcasting Corporation Stations: KBJZ-LPFM 94.1 Address: PO Box 20247, Juneau, AK 99801 Phone: 907-586-3941

ANNEX E

JUNEAU AREA LOCAL EMERGENCY COMMUNICATIONS COMMITTEE

Dennis Egan, Chair KINY 907-586-6037 egan@ptialaska.net

Bill Legere KTOO 907-586-1670 bill@ktoo.org

Michael Patterson City and Borough of Juneau 907-586-0221 michael_patterson@ci.juneau.ak.us

Joel Curtis National Weather Service 907-790-6803 joel.curtis@noaa.gov

Tom Ainsworth National Weather Service 907-790-6804 tom.ainsworth@noaa.gov

Chief Eric Mohrmann Capital City Fire Rescue 907-586-0261 eric_mohrmann@ci.juneau.ak.us

Chief Greg Browning Juneau Police Department 907-586-0677 gbrowning@juneaupolice.com

Warren Russell GCI Cable 907-463-1444 wjrussell@gci.com

Rob Knorr GCI Cable 907-463-1410 rknorr@gci.com

Scott Willis Alaska Electric Light and Power 907-780-2222 scott.willis@aelp.com

ANNEX F

ACRONYMS

C.F.R. 	Code of Federal Regulations

CBJ 	City and Borough of Juneau

EAS 	Emergency Alert System

EOM 	End of Message

FCC 	Federal Communications Commission

LECC 	Local Emergency Communications Committee

LP-(1,2,3) 	Local Primary (1,2,3)

NWS 	National Weather Service

U.S.C. 	United States Code

# Text boxes

A WORD OF CAUTION: The Emergency Management/Services community has acquired a valuable new tool in gaining direct access to all area broadcasters and subject cable operators via the EAS. However, if not used prudently, you put yourself in danger of losing this tool. Broadcasters and cable operators are expecting the EAS to be used only for very serious emergencies. Keep in mind two things. First, some broadcasters and cable operators have their EAS decoders set on Automatic Mode. There will be no one there to screen your message and decide if it should be aired. They are depending on you to send an EAS Alert only for a very serious emergency. The first time you trigger the system for a frivolous event, you will lose the confidence of your area broadcasters and cable operators.  The second thing to remember is that broadcasters and cable operators participate in the local level EAS on a voluntary basis. No one can force them to carry out your EAS Alerts. Maintain a good relationship with your local broadcasters and cable operators, and they will come through for you in a crisis.