Alaska Statewide Debris Management Planning Project

Task 3: HAZUS GIS Debris Estimation Models Report

August 2009

TABLE OF CONTENTS

1.	Debris Totals by Event and Type	1-1

1.1	Earthquake Event	1-1

1.2	Flood Event	1-2

1.3	Tsunami Event	1-3

2.	Debris Estimates	2-1

3.	Anomalies, Errors, and Work-Arounds	3-1

Tables

1. 	Estimated Debris Totals (Cubic Yards)	1-1

2. 	Earthquake Event Inputs	1-2

3. 	Coastal Event Input Values (Feet)	1-3

4. 	Tsunami Still-Water Elevations	1-3

5. 	MRLC Woodland Landcover Classes	2-1

Figures

1. 	Woodland MRLC Raster	2-2

2. 	Woodland MRLC by Tract	2-3

3. 	FIADB by Jurisdiction	2-3

4. 	Soil Class by Jurisdiction	2-4

5. 	Slope Class by Jurisdiction	2-4

6. 	Erosion Susceptibility	2-5

7. 	Impacted Acreage Estimate	2-6

Appendices

A	Anchorage

B	Juneau

C	Sitka

D	Kenai Peninsula

E	Matanuska-Susitna

F	Fairbanks Northstar

G	Ketchikan Gateway

H	Kodiak Island

ACRONYMS

DEM		Digital Elevation Model

ERDAS	Earth Resources Data Analysis System

FEMA	U.S. Department of Homeland Security’s Federal Emergency Management Agency

FIADB		Forest Inventory and Analysis Database

FIS		Flood Insurance Study

MRLC		Multi-Resolution Land Cover

NRCS		Natural Resources Conservation Service

STATSGO	State Soil Geographic Database

SWE		still-water elevation

USGS		U.S. Geological Survey

# Debris Totals by Event and Type

HAZUS-MH is the U.S. Department of Homeland Security’s Federal Emergency Management Agency (FEMA’s) Hazards U.S. risk assessment software program used to analyze potential losses from different hazard scenarios. In HAZUS-MH, current scientific and engineering knowledge is coupled with the latest geographic information systems (GIS) technology to produce estimates of hazard-related damage before, or after, a disaster occurs. HAZUS-MH estimates disaster-generated debris through three models: earthquake tsunami, and flood. These models are periodically revised and updated through input from engineers, scientists, software developers, and hazards specialists to provide best available loss estimates base on input data.

Preliminary debris estimates were calculated using source data from various governmental agencies and geographical databases for eight jurisdictions within Alaska. Table 1 and Appendices A-H show the estimated debris totals by jurisdiction for earthquake, flood, and tsunami events.

| Table 1. Estimated Debris Totals (Cubic Yards) |
| --- |
|  | Earthquake | Flood (Combined) | Tsunami |
| Jurisdiction | CW | CD | CW | CD | CW | CD |
| Anchorage | 364,637 | 4,716,801 | 2,214 | 86,143 | 14,893 | 15,136 |
| Juneau | 71,371 | 287,080 | 31,120 | 1,131,921 | 1,222 | 13,785 |
| Sitka | 69,898 | 165,817 | 13,331 | 117,549 | 990 | 9,040 |
| Kenai | 46,244 | 448,144 | 27,817 | 336,481 | 471,057 | 375,014 |
| Mat-Su | 35,457 | 35,457 | 41,176 | 86,143 | 14,893 | 15,136 |
| Fairbanks | 139,580 | 1,787,509 | 84,422 | 222,235 | N/A | N/A |
| Ketchikan | 5,511 | 32,008 | 25,228 | 32,008 | * | * |
| Kodiak | 2,298 | 203,874 | 65,858 | 146,786 | 105,839 | 371,429 |
| † Estimate calculation based on an analogous jurisdiction; see Section 1.2. * Input parameters were insufficient to produce valid model output; see Section 1.3. |
| CD = construction and demolition debris CW = clean-wood debris |

## Earthquake Event

The earthquake event was modeled for each jurisdiction using a moment magnitude of 8.5 (HAZUS maximum value) and an epicenter located within 100 miles of each jurisdiction along an easily recognizable historical fault. Table 2 summarizes earthquake event inputs.

| Table 2. Earthquake Event Inputs |
| --- |
| Jurisdiction | Attenuation Model | Epicenter Lat | Epicenter Long | Moment Magnitude | Fault Depth (miles) | Fault Width (miles) |
| Anchorage | Youngs, et al. | 61.25 | -150.75 | 8.5 | 15.5 | 6.2 |
| Juneau | Youngs, et al. | 57.69 | -136.07 | 8.5 | 15.5 | 6.2 |
| Sitka | Youngs, et al. | 56.77 | -135.91 | 8.5 | 15.5 | 6.2 |
| Kenai | Youngs, et al. | 60.15 | -152.82 | 8.5 | 15.5 | 6.2 |
| Mat-Su | Youngs, et al. | 61.25 | -150.75 | 8.5 | 15.5 | 6.2 |
| Fairbanks | Youngs, et al. | 64.6 | -147.1 | 8.5 | 15.5 | 6.2 |
| Ketchikan | Youngs, et al. | 55.09 | -134.13 | 8.5 | 15.5 | 6.2 |
| Kodiak | Youngs, et al. | 58.29 | -125.5 | 8.5 | 15.5 | 6.2 |
| Youngs, R.R., et al. 1997. Strong Ground Motion Attenuation Relationships for Subduction Zone Earthquakes. Seismological Research Letters 68(1). |

## Flood Event

A 500-year flood event was modeled for each identified jurisdiction for both riverine and coastal flood scenarios (where applicable).

Because of HAZUS data limitations, the riverine scenario was modeled using an average discharge value from the FEMA Flood Insurance Study (FIS) for each jurisdiction, or the HAZUS default value when no FIS was available. Initially, U.S. Geological Survey (USGS) National Elevation Dataset Digital Elevation Model (DEM) data were used to calculate stream reaches within a 10-mile area around each identified jurisdiction. However, it quickly became apparent that for the larger jurisdictions (e.g., Matanuska-Susitna Borough) the processing time required was extremely cumbersome (approximately nine days for each of three attempts) and yielded no useable results. After adjustment of the reach parameter to a maximum of 2.5 miles in populated areas, the results were determined to be more useable.

Coastal flood scenarios were run using input variables, including wave exposure, shoreline type, and still-water elevation (SWE), obtained from the National Oceanic and Atmospheric Administration (Alaska ShoreZone data) and FEMA FISs (Table 3). Where the SWE value exceeded the HAZUS maximum, the HAZUS maximum was used, and where these values were missing from the FIS, the HAZUS-calculated value was used.

| Table 3. Coastal Event Input Values (Feet) |
| --- |
| Jurisdiction | Wave Exposure | Shoreline Type | 100-year SWE | Wave Setup | 10-year SWE | 50-year SWE | 500-year SWE |
| Anchorage | Sheltered | Open wetlands | 15.3 | No | 13.7 | 14.1 | 18.1 |
| Juneau | Sheltered | Open wetlands | 30.0 | No | 15.0 | 25.0 | 35.0 |
| Sitka | Minimal exposure | Sandy beach, small dunes | 20.6 | No | 15.0 | 20.3 | 21.7 |
| Kenai | Moderate exposure | Sandy bluffs, little beach | 15.3 | No | 13.7 | 14.1 | 18.1 |
| Mat-Su | Sheltered | Open wetlands | 15.3 | No | 13.7 |  |  |
| Fairbanks | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| Ketchikan | Sheltered | Sandy beach, small dunes | 30.0 | No | 15.0 | 25.0 | 35.0 |
| Kodiak | Moderate exposure | Sandy beach, small dunes | 29.0 | No | 15.0 | 25.0 | 29.6 |
|  | = HAZUS maximum |
|  | = HAZUS calculated |
| N/A = not available SWE = still-water elevation |

## Tsunami Event

The tsunami event was modeled based on a 500-year return interval coastal flood event using SWEs from historical records of the 1964 Great Alaskan Earthquake at or near each applicable jurisdiction (Table 4).

| Table 4. Tsunami Still-Water Elevations |
| --- |
| Impact Location | Latitude | Longitude | Height (feet) |
| Juneau | 58.30 | -134.42 | 3.61 |
| Ketchikan | 55.33 | -131.63 | 1.97 |
| Homer1, 2 | 59.68 | -151.61 | 19.69 |
| Halibut Cove2 | 59.34 | -151.50 | 23.62 |
| Seldovia2 | 59.47 | -151.68 | 3.94 |
| Kodiak3 | 57.81 | -152.40 | 20.01 |
| Narrow Cape3 | 57.43 | -152.33 | 62.34 |
| Women's Bay3 | 57.73 | -152.52 | 20.01 |
| Kaguyak3 | 56.83 | -153.83 | 30.18 |
| Old Harbor3 | 57.22 | -153.37 | 30.18 |
| Sitka | 57.08 | -135.33 | 7.87 |
| 1 Used for Municipality of Anchorage and Matanuska-Susitna Borough as a close approximation. 2 Average of values used for Kenai Peninsula Borough. 3 Average of values used for Kodiak Island Borough. |

This page left blank intentionally

# Debris Estimates

The amount of construction and demolition debris was estimated using default data included with HAZUS, which include two general categories; (1) brick, wood, and others and (2) concrete and steel. Due to limitations in HAZUS, clean-wood debris estimates are only available in the hurricane model (which is only offered for the East Coast). To remedy this limitation, clean-wood debris were estimated using debris inventories developed according to the HAZUS hurricane model method, which uses vegetation data derived from re-classification of USGS Multi-Resolution Land Cover (MRLC) data and U.S. Forest Service Inventory and Analysis Database (FIADB) data. Using overlay spatial analysis techniques, Natural Resources Conservation Service (NRCS) State Soil Geographic Database (STATSGO) and USGS DEM data were processed to yield areas vulnerable to debris generation. These areas were then used in each event run to provide clean-wood debris estimates.

The Alaska statewide MRLC dataset is distributed by download as an Earth Resources Data Analysis System (ERDAS) Imagine raster dataset (.img), which is clipped to the “envelope” (i.e., the bounding extents) of each jurisdiction and then converted to ArcInfo raster GRID format. Using the HAZUS-based jurisdictional boundaries, each GRID was extracted to the more precise boundary of each jurisdiction and reclassified to isolate “woodland pixels,” which are a subset of the MRLC classification based on HAZUS parameters (Table 5).

| Table 5. MRLC Woodland Landcover Classes |
| --- |
| Type | Grid Code | Effective Area (%) |
| Deciduous forest | 41 | 100 |
| Coniferous (evergreen) forest | 42 | 100 |
| Mixed forest | 43 | 100 |
| Woody wetlands | 90 | 100 |
| Developed, low intensity | 22 | 20 |
| Developed, medium intensity1 | 23 | 15 |
| Developed, high intensity | 24 | 10 |
| 1 Not present in the HAZUS specification but estimated between high and low intensity. MRLC = Multi-Resolution Land Cover |

The woodland landcover class types were added to the extracted jurisdiction subset rasters to create woodland MRLC rasters by jurisdiction (Figure 1).

Figure 1. Woodland MRLC Raster

The woodland MRLC rasters then were converted to vector datasets and three attribute fields, (1) ACRES, (2) ADJ, and (3) ACRES_ADJ, were added to each jurisdiction vector landcover dataset. ACRES, the acreage of each vector polygon, was calculated using an internal ArcGIS utility; ADJ, a percentage of woodlands adjustment, was populated based on the effective area of each landcover type (see Table 5); and ACRES_ADJ was calculated by multiplying ACRES by ADJ (Figure 2).

Figure 2. Woodland MRLC by Tract

The vector landcover for each jurisdiction was then combined using the union function with HAZUS-based census tracts for each jurisdiction to yield woodland MRLC by tract.

The FIADB is available via a U.S. Forest Service download and is composed of over 40 tables. The TREE and PLOT tables provide density, diameter, and height information per plot. These tables were accessed, joined, and geocoded based on the latitude and longitude values from the PLOT table. The TREE and PLOT tables were then intersected with each jurisdiction boundary, subseted, and exported to the project database (Figure 3).

Figure 3. FIADB by Jurisdiction

The NRCS SSURGO soils data were unavailable for all jurisdictional areas, so to generate a consistent erosion susceptibility factor raster overlay, statewide NRCS STATSGO soils data were used. An erodibility factor attribute, KFFACT, was used to reclassify rasterized (converted to raster) soil type areas into low (0.0–0.28), moderate (0.32–0.43), and high (0.49–0.64) classes (Figure 4).

Figure 4. Soil Class by Jurisdiction

USGS DEM data were extracted from the USGS National Map Seamless Server for each jurisdiction and geoprocessed to generate percent slope rasters. The percent slope rasters were then reclassified into low (<1.5 percent), moderate (1.5-15 percent), and high (>15 percent) classes (Figure 5).

Figure 5. Slope Class by Jurisdiction

The soil class and slope class datasets were combined in an additive raster overlay to yield the final erosion susceptibility raster. Cell values ranged from 2 to 6 (low to high) (Figure 6).

Figure 6. Erosion Susceptibility

Riverine, coastal, and tsunami events were modeled in HAZUS to generate geospatial inundation boundaries, (i.e., the extent to which flood waters would inundate the surrounding land). Riverine and coastal flood events were merged to produce a combined flood event for each jurisdiction. From these inundation boundaries, the erosion susceptibility data were extracted to yield the susceptible areas inundated by each event. These datasets were converted to vector (polygon) format and attribute-intersected (identity function) with the woodland MRLC by tract for each jurisdiction to produce an inundated, erosion susceptible dataset by MRLC landcover type and census tract. The number of acres for each vector polygon was re-calculated based on dataset geometry and the ADJ was then re-applied. The erosion-susceptibility values were converted to a percentage (20–50 percent) and multiplied by the adjusted acres to calculate the acres impacted by each event.

The number of impacted acres for each event in each jurisdiction was summarized by census tract. The average trees per acre was calculated for each jurisdiction based on the FIADB subset and applied to the impacted acres to produced average cubic feet of natural debris generated by each event in each jurisdiction, as shown in Figure 7.

Figure 7. Impacted Acreage Estimate

To estimate the natural debris generated by an earthquake event, the percent of woodlands was calculated by tract using the MRLC by tract ACRES_ADJ value. A vegetation multiplier was apply based on low (1.0 for 0–33 percent), moderate (1.2 for 33–66 percent), and high (1.3 for 66–100 percent) percent woodlands. An estimate of the average cubic feet of debris per acre was calculated from the non-structural or foundational debris estimated by HAZUS. This value was applied to the adjusted acres and multiplied by the applicable vegetation multiplier to yield total cubic feet of debris per acre, summarized by tract, for each jurisdiction.

# Anomalies, Errors, and Work-Arounds

The models used by HAZUS incorporate state-of-the-art methods and robust data processing algorithms. This combination of components had proven to yield relevant, balanced, and consistent results across a wide range of disaster scenarios. However, model output can, at best, only match the standard of the data input within the parameter options of the model. Certain anomalies and errors have been discovered in the modeling of the tsunami (coastal) and riverine flood events for certain jurisdictions. Two types of anomalies were generated. The first type of anomaly was generated because the input parameter options were too low to produce valid output (see Ketchikan in Table 1 and Table 4). The second type of anomaly was generated because of the input data resolution and a geospatial phenomenon known as the Modifiable Area Unit Problem, which is present when data are distributed across a highly variable set of area units (in this case census tracts) that actually only occurs in a very limited sub-section of the given area unit. This anomaly can yield calculations that seem much lower or much higher than is reasonable for a given area.

Besides anomalous results, a system error was generated due to a large jurisdictional area input parameter option and idiosyncrasies in computer system hardware and software configurations. Large jurisdictional area riverine event modeling utilized a user input DEM (see Section 1.2) with an approximate pixel resolution of 60 meters (2 arc seconds, horizontal). In HAZUS, an elevation surface was generated to calculate each stream reach and each reach inundation boundary based on input parameter options. Large jurisdictional areas (e.g., Matanuska-Susitna Borough) require a highly refined selection of input data and parameter options that could not be achieved under the scope of this project. The work-around for this error was to examine an analogous jurisdiction, with a similar level of infrastructure, and make estimates based on the relationships between debris types.

# Text boxes

Woodland Landcover Classes

MRLC Gridcode

Extract by Mask

Convert to Vector

MRLC GRID by Jurisdiction

Convert to GRID

Raster Clip

Jurisdictional Boundary

Statewide MRLC

Attribute Join

Woodland MRLC Raster

Woodland MRLC Raster

Woodland MRLC Vector

Add & Calculate: ACRES, ADJ, ACRES_ADJ

Union

HAZUS Census Tracts by Jurisdiction

Woodland MRLC by tract

FIADB by Jurisdiction

Intersect & Subset

Jurisdictional Boundary

Geocode

Attribute Join

PLOT

TREE

FIADB

Percent Slope Raster by Jurisdiction

Slope Class by Jurisdiction

Reclassify

DEM by Jurisdiction

Percent Slope

USGS Seamless Server

Soil Class by Jurisdiction

Reclassify

Clip

Jurisdictional Boundary

Join KFFACT

Statewide NRCS Soils

Convert to Raster

Soil Class by Jurisdiction

Slope Class by Jurisdiction

Raster Plus

Erosion Susceptibility

HAZUS Riverine Inundation Bounds

HAZUS Coastal Inundation Bounds

HAZUS Combined Inundation Bounds

Merge

Erosion Susceptibility

Extract by Mask

Convert to Vector

Woodland MRLC by tract

Identity

Susceptible Areas Inundated by Jurisdiction

Recalculate:

ACRES, ACRES_ADJ;

Add & Calculate Field: ACRES_IMPACT

Inundated, Erosion Susceptible, MRLC by tract